## Slide 1: Basic Principles of Dialysis Hemodialysis Solute Transport and Assessment of Adequacy
Brent W. Miller, MD
Indiana University School of Medicine
Dialysis Core Curriculum 2021

## Slide 2: Brent W. Miller
Employer: Indiana University
Consultancy Agreements: Fresenius Kidney Care
Honoraria: UpToDate, Davita, Home Dialysis University, Fresenius Renal Therapies Group, Advanced Renal Education Program, University of Southern California
Scientific Advisor or Membership: NxStage Medical Scientific Advisory Board
Other Interests: Author, UpToDate in Medicine
Disclosures
Dialysis Core Curriculum 2021

## Slide 3: Learning Objectives
Explain how key solutes are removed during hemodialysis
Identify how to measure solute removal and adjust the hemodialysis prescription
Describe solute removal and correction of uremic symptoms
Discuss the various definitions of adequate hemodialysis
  Regulatory
  Clinical
Dialysis Core Curriculum 2021

## Slide 4: Outline
Brief review of general solute removal principles
Specific clinical issues
  Sodium
  Potassium
  Phosphorus
  Calcium
  Acid
  Medium and Large Molecules
  Protein-Bound Molecules
Assessing the clinical efficacy of hemodialysis (“Adequacy”)
  Brief History and Scientific Background
  Clinical Definitions and Adjustments
  Regulatory Definitions
Dialysis Core Curriculum 2021

## Slide 5
General Principles
(Please also see Dr. Clark’s section)
Solute Transport
Dialysis Core Curriculum 2021

## Slide 6: Principles of Dialysis
General Principles
Diffusion
Osmosis
Solvent drag
Hydrostatic Pressure
Ultrafiltration
Semi-permeable membrane
Solution A
Solution B
Solute Removal = Diffusion + Convection + Absorption
Clinically relevant removal of uremic solute = Diffusion + Convection
Dialysis Core Curriculum 2021
Notes: Dialysis involves the movement of particles from 2 liquids separated by a semi-permeable membrane. In the clinical setting with patients experiencing kidney failure, the liquids are the blood and the dialysis solution with the blood moving on the inside of a hollow fiber and the dialysis fluid surrounding the hollow fiber. The forces that typically drive movement across the membrane are osmosis, diffusion, hydrostatic pressure on one side of the membrane causing ultrafiltration, and solvent drag. The clinically relevant removal of uremic solutes involves diffusion of these molecules across the membrane and the concentration gradient and convection of uremic solutes following the movement of water or plasma via ultrafiltration with pressure applied to one side of the membrane and solvent drag as water and plasma move across the osmotic gradient. The movement depends upon characteristics of the specific solute and the specific membrane. In general, smaller molecules are moved more by diffusion and larger molecule removal depends more on convection. This is one of the reasons for the interest in hemofiltration, hemodiafiltration and higher cut-off dialysis membranes. The historical United States practice has been largely diffusive removal of uremic solutes with an emphasis on urea removal as a surrogate for the amount of dialysis performed.
Some experimental therapies have utilized absorptive columns with the dialysis membrane for further solute removal and some have utilized living renal tubular cells in dialysis membranes for further metabolism and clearance.

## Slide 7: The Hemodialysis Circuit
Water Circuit
Dialysate Components
Dialysate Heater
Semipermeable Membrane
Balancing Chamber
Blood Pump
Anticoagulation
Air Chamber
General Principles
Dialysis Core Curriculum 2021

## Slide 8: Dialyzer Clearance (K)
Depends upon the blood flow rate (Qb)
Depends upon the dialysate flow rate (Qd)
Note that dialysis clearance can never exceed Qb or Qd. (This becomes particularly relevant with lower dialysate flow systems. For example, if 20L of dialysate is utilized, then the maximum clearance of a solute is 20L.)
The practical maximum in vivo clearance rate of small solutes occurs at a Qd/Qb of 1.5-2.0.
Practical considerations
  The impact of non-plasma or cellular portions of blood is not accounted for.
  Most reported dialyzer clearances are done in vitro with cell-free solute.
  The blood pump speed may not accurately reflect blood delivery to the dialyzer.
General Principles
Dialysis Core Curriculum 2021

## Slide 9: Mass Transfer Coefficient (Ko)
Different for each solute
When multiplied with surface area of a membrane (KoA), it is an alternative to measured clearance.
General Principles
Dialysis Core Curriculum 2021

## Slide 10: Ultrafiltration Coefficient (Kuf)
Measures dialysis membrane permeability to water
Historically was important because of ultrafiltration control prior to dialysis machines with volumetric control
Now utilized to define high-efficiency vs. high-flux dialyzers
General Principles
Dialysis Core Curriculum 2021

## Slide 11: High Efficiency vs. High Flux*
Ultrafiltration coefficient (Kuf) >15 ml/h/mm Hg transmembrane pressure (TMP)
Larger pore size
B2 microglobulin clearance >20 ml/min
Ultrafiltration coefficient (Kuf) <15 ml/h/mm Hg TMP
Smaller pore size
Large surface areas
B2 microglobulin clearance variable, often <10 ml/min
General Principles
High Efficiency
High Flux
* Due to both technological improvements and decreased cost of manufacturing, the majority of dialysis membranes in the U.S. now are made of components that have high-flux characteristics.
Dialysis Core Curriculum 2021

## Slide 12
Sodium
Solute Transport
Dialysis Core Curriculum 2021

## Slide 13: The Negative Impact of Too Much Dietary Sodium Intake Cannot Be Overemphasized and Overwhelms the Best Hemodialysis Prescription and Treatment
Retrospective analysis of 1770 subjects in HEMO trial
Reported sodium intake in quartiles
Adjusted for age, sex, race, weight, access, CHF, DM, CAD, sodium, albumin, creatinine, UF, caloric intake, and protein intake
Sodium
Chart: Mortality Hazard Ratio
| Unadjusted | Adjusted
Q1 | 1 | 1
Q2 | 1.12 | 1.16
Q3 | 1.08 | 1.23
Q4 | 0.96 | 1.39
Adapted from McCausland FR et al. Kidney Int 82:204, 2012
Dialysis Core Curriculum 2021

## Slide 14: Sodium Removal in HD vs. PD
Sodium removal is different between peritoneal and hemodialysis.
  Approximately 80% of sodium removal in hemodialysis is via convection (ultrafiltration) and 20% via diffusion.
    The correct target weight, rather than the sodium gradient, per se, is the most critical part of the prescription for sodium removal.
    The sodium bath can be varied with unintended consequences. (see later slides)
  In contrast, diffusion is much more important for sodium removal with peritoneal dialysis, usually accounting for approximately 1/3 of the total amount.
    CAPD typically removes more than CCPD.
    Short dwell times on CCPD can lead to more free water transport than sodium removal; hence, the term “sodium sieving.”
    Attempts to increase the sodium gradient and enhance sodium diffusion come at the expense of decreased ultrafiltration due to the decline in osmolarity.
Sodium
Dialysis Core Curriculum 2021

## Slide 15: Choice of Sodium Dialysate Bath* (Most patients tolerate dialysate [Na+] >135 mmol/L well)
 | Pros | Cons
Higher Sodium Bath | Less hypotensive episodes Less dialysis symptoms Decrease in intracellular water | Stimulation of thirst Increased intradialytic weight gain Total body sodium retention
Lower Sodium Bath | Increased diffusive removal of sodium Less risk of hypertension Less risk of chronic volume overload | Risk of hypotension Increased intracellular water Increased symptoms with dialysis Chronic hyponatremia has been associated with mortality in HD
Sodium
* While most patients in the U.S. are on a fixed sodium dialysate bath and studies with variable sodium dialysate baths don’t show consistent improvements, individual patients may benefit from a variable bath.
Dialysis Core Curriculum 2021

## Slide 16
Potassium
Solute Transport
Dialysis Core Curriculum 2021

## Slide 17: How Potassium Is Handled During Hemodialysis Has Dramatic Consequences
High potassium is potentially lethal.
Low potassium is potentially lethal.
Intradialytic potassium handling likely has serious consequences.
  Low potassium baths (i.e., high potassium gradients) have been associated with mortality.
  Rapid correction of alkalosis during hemodialysis has been associated with mortality presumably due to rapid lowering of plasma potassium.
Potassium
Dialysis Core Curriculum 2021

## Slide 18: Serious Consequences of Potassium Disorders
Potassium
Kovesdy CP, Clin J Am Soc Nephrol 2:999, 2007
Dialysis Core Curriculum 2021

## Slide 19: Potassium Homeostasis in ESRD
Total body K is 50-55 mEq/kg.
Approximately 90-98% is intracellular.
0.4% is in plasma.
Approximately 95% is interchangeable.
60-75% is in muscle (followed by liver and RBCs).
Normal K intake is 0.75-1.0 mEq/kg/day.
Normal kidney removes 95% of dietary K; 5% GI excretion.
In ESRD, GI removes 35% of K load, 6-8 hours after intake via increased colonic secretion.
Thus, dialysis must remove 40-70 mEq/day or 80-140 mEq/ HD session in 3x week.
Potassium
Rachoin JS and Weisberg LS Sem Dial 21:223, 2008
Denicola L et al. J Am Soc Nephrol 11:2337, 2000
Zehnder C et al. Nephrol Dial Transplant 16: 78, 2001
Martin RS et al. Am J Kidney Dis 8:105, 1986
Sandle GI et al. Clin Sci 73:247, 1987
Navarro MP and Vaquero MP. Encyclopedia of Food Sciences 2003
Dialysis Core Curriculum 2021

## Slide 20: Potassium Homeostasis in ESRD
Potassium
Chart: PERCENT
| PD Low K | HD Low K | PD High K | HD High K
Series 1 | 15 | 0.5 | 0.8 | 10
Adapted from Choi HY and Ha SK. Electrolyte Blood Press 11:9-16, 2013 and Oreopoulus D et al. Nephron 30: 293, 1982
Dialysis Core Curriculum 2021

## Slide 21: Potassium Removal During Hemodialysis
Approximately 85% of potassium removal is via diffusion.
  Typical hemodialysis removal rate=0.3 meq/kg/hour, but not linear
  Typical peritoneal dialysis removal rate=0.02 meq/kg/hour
Therefore, the blood:dialysate gradient determines removal.
First 25% of hemodialysis treatment: Potassium from intravascular and extracellular compartment exponentially declines
Last 75% of hemodialysis: 60% from intracellular compartment
6 hours after HD: Another significant shift of potassium from intracellular compartment to extracellular and intravascular compartment: Potassium Excursion (see next slide)
In contrast, PD has no potassium excursion and almost all potassium removed comes from the intracellular compartment and the potassium level is near constant.
Potassium
Dialysis Core Curriculum 2021

## Slide 22: Typical Potassium Removal with HD
Chart: Hours Since Initiation of Hemodialysis
| 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10
Plasma Potassium | 5.6 | 4.3 | 3.8 | 3.5 | 3.4 | 4.2 | 4.3 | 4.4 | 4.5 | 4.7 | 4.8
Potassium
Adapted from the work of Blumberg A, et al. Nephrol Dial Transplant 12:1629-1634, 1997 and others
Hemodialysis
Rebound
Dialysis Core Curriculum 2021

## Slide 23: What Is the Role of Dietary Restriction and Gastrointestinal Potassium Binders?
The overwhelming majority of hemodialysis patients require a dietary potassium restriction between 0.4-0.8 meq/kg/day to be followed by a renal dietitian in consultation with the nephrologist.
The role of chronic use of oral potassium binding agents in hemodialysis patients is still being defined.
  Patiromer
  Sodium Zirconium Cyclosilicate
POTASSIUM
Dialysis Core Curriculum 2021

## Slide 24
Phosphorus
Solute Transport
Dialysis Core Curriculum 2021

## Slide 25: Overview of Phosphorus Removal with Hemodialysis
Removal of phosphorus during hemodialysis is complex.
Phosphorus removal is more amenable to time on hemodialysis than other similar small solutes.
  Mass balance studies over 40 years have shown substantial removal of phosphorus during the later stages of hemodialysis treatments.
  Physiological demonstration of this principle came from low volume (<50L diaylsate), nocturnal hemodialysis in the 1990s.
Phosphorus
Dialysis Core Curriculum 2021

## Slide 26: Phosphorus Removal with Time on Hemodialysis
Phosphorus
Adapted from Skrabal F et al. Klin Wschr 52:266, 1974
Chart: Hours Since Hemodialysis Initiation
| 2 | 4 | 6 | 8
4.0 meq/L Ca+ bath | 319 | 256 | 243 | 199
3.0 meq/L Ca+ bath | 214 | 207 | 219 | 216
Note that phosphorus removal continues briskly with time and that calcium concentration in dialysate affects removal.
Dialysis Core Curriculum 2021

## Slide 27: Phosphorus Removal and Dialysis Time
Chart: Mass removed with a single hemodialysis treatment
| Phosphorus Removal | Urea Removal
Conventional | 25.3 | 470
Nocturnal | 26.9 | 315
Phosphorus
Adapted from Musci I, Hercz G, Uldall R, Ouwendyk M, Francoeur R and Pierratos A. Kidney Int 53:1399-1404, 1998
Note Relative Difference
Time allows more movement of phosphorus into vascular space and removal by dialysis.
Dialysis Core Curriculum 2021
Notes: These treatments were not controlled for time only. Note that the shorter treatment has a larger dialysis membrane surface area, higher blood flows and dramatically more dialysate flow and thus total dialysate volume. Therefore, the relationship between time and phosphorus removal stands out. The next slide shows recent work why this is true: phosphorus is being mobilized from intracellular spaces.

## Slide 28: Phosphorus Removal and Dialysis Time
Phosphorus
Note phosphate removal continues significantly with time and a significant amount of phosphate comes from the intracellular compartment
Dialysis Core Curriculum 2021
Chabot G et al. J Am Soc Nephrol 2020. doi: https://doi.org/10.1681/ASN.2020050716
Notes: The graph on the left demonstrates phosphate removal during remaining brisk as hemodialysis continues. The graph on the right shows an increase in the phosphocreatinine to inorganic phosphate ratio during hemodialysis, which implies depletion of intracellular phosphate.

## Slide 29
Calcium
Solute Transport
Dialysis Core Curriculum 2021

## Slide 30: Calcium Mass Balance During Hemodialysis
Calcium flux in hemodialysis is also complex.
  Calcium concentrations can change during hemodialysis.
  Gibbs-Donnan equilibrium affects behavior at dialysis membrane.
  Commonly-used medications affect plasma calcium level and thus gradient.
Caution should be exercised with either high (positive balance) or low (negative balance) dialysate baths.
  Positive balance is potentially associated with hypercalcemia and vascular calcification.
  Negative balance is potentially associated with bone loss, hemodynamic instability and cardiac dysrhythmias.
Calcium
Dialysis Core Curriculum 2021

## Slide 31: Factors Affecting Calcium Mass Balance During HD
Plasma-Dialysate Gradient
Flux across dialysis membrane
  Blood flow rate
  Dialysate flow rate
  Gibbs-Donnan effect
Serum phosphorus concentration during treatment
Flux of calcium from bone to plasma during treatment
  PTH level
  Osteocalcin level
Calcium
Dialysis Core Curriculum 2021

## Slide 32: Historic Calcium Mass Balance During Hemodialysis
Calcium
Adapted from Hou S et al. Am J Kidney Dis 18:217, 1991
Qd= 500 ml/min (120 L dialysate)
Qb=300 ml/min
1.0m2 membrane (TAF10)
4-hour treatment
Maximal UF 3.6L
Total Calcium Balance
3.5 mEq/L = +879 mg
2.5 mEq/L = +216 mg
1.5 mEq/L = -231 mg
Note that calcium flux changes with low calcium dialysate bath over the course of a treatment, likely due to the changes in plasma phosphorus concentration whereas the calcium mass transfer is stable throughout the treatment with higher calcium baths.
Dialysis Core Curriculum 2021

## Slide 33: Calcium Mass Balance During Hemodialysis
Calcium
Adapted from Karohl et al. Nephrol Dial Transplant 25:1244, 2010
Dialysate Bath | Mean Balance (mg) | Median Balance (mg)
3.5 mEq/L | 405 + 413 | 268
3.0 mEq/L | 46 + 400 | -46
2.5 mEq/L | -468 + 563 | -468
2.0 mEq/L | -578 + 389 | -492
Note large standard deviation and the subsequent complexity of a scatter plot. Therefore, it is hard to know what the exact calcium balance in an individual patient will be during a hemodialysis treatment. Proceed with caution with very high or very low dialysate calcium concentrations.
Dialysis Core Curriculum 2021

## Slide 34
Acid Base
Solute Transport
Dialysis Core Curriculum 2021

## Slide 35: Acid Base
Choice of buffer
  Acetate: no longer utilized due to patient symptoms during dialysis
  Lactate
  Bicarbonate:
    Well tolerated
    Concerns with stability, interaction with calcium and microbiological growth
Degree and rate of acidosis correction
  Under-correction of acidosis can affect bone and muscle structure and function.
  Overcorrection, particularly when combined with transient hypokalemia, may impact cardiac function and dysrhythmia.
Is there a role for oral base supplementation between dialysis sessions?
Is there a role for lowering bicarbonate bath concentration in ventilated, critically ill patients with acute lung injury to prevent further CO2 retention?
Dialysis Core Curriculum 2021

## Slide 36
Medium and Large Molecules
Solute Transport
Dialysis Core Curriculum 2021

## Slide 37: Medium and Large Molecules
In general, the clearance of medium-sized and large-sized, non-protein bound solutes at normal operating conditions is dependent upon length of dialysis.
  Minimal increase in removal when increasing Qd from 300 ml/min to 800 ml/min
  The exact role of these uremic retention solutes has not been elucidated.
  Routine clinical measurement of these solutes is not performed.
This is also true for peritoneal dialysis.
Protein-bound molecules may benefit from higher dialysate flows.
Dialysis Core Curriculum 2021

## Slide 38
Safety
Solute Transport
Dialysis Core Curriculum 2021

## Slide 39: Safety
Potential removal of beneficial substances
  Water soluble vitamins
  Other molecules (e.g., levocarnitine, etc.)
Potential inward transport of harmful substances
  Aluminum
  Nitrites
  Chloramines
  Many others
Dialysis Core Curriculum 2021

## Slide 40
History
Assessing Adequacy
Dialysis Core Curriculum 2021

## Slide 41: Overview of Assessing Dialysis Adequacy
Clinical signs and symptoms always outweigh any biochemical measure of dialysis adequacy.
Urea, a small molecule, has been and will remain the standard for measurement of dialysis for the foreseeable future.
  A better measure has not been identified.
  Reimbursement has been tied to obtaining urea clearance metrics.
Urea is not an absolute uremic toxin by itself.
  Addition studies in the 1970s
  HEMO study in the 1990s
There is not a linear relationship between urea kinetics and clinical outcomes. (e.g., KtVurea of 1.2 is not necessarily “better” than 1.4)
History
Dialysis Core Curriculum 2021

## Slide 42: Measures of Dialysis Adequacy Are Tools
History
“The parameters Kt/V, nPCR, and EKR help dialysis care givers focus on patients whose prescriptions, including their dialysis schedule, time on dialysis, dialyzer clearance, and dietary protein need adjustment.”
Dr. Tom Depner in Principles and Practice of Dialysis, 1999
Dialysis Core Curriculum 2021

## Slide 43: NCDS Study 1981: Beginning of a “Dialysis Dose”
History
Hypothesis was that lowering peak urea concentration from 100 mg/dl to 50 mg/dl would improve outcomes.
This did not affect outcomes; however:
  Urea Reduction Ratio (URR) did have an effect.
  Subsequent analysis showed a significant difference between Kt/Vurea of <0.8 and >1.0.
In this very small study, dialysis time was not quite statistically significant (p=0.06).
Dialysis Core Curriculum 2021

## Slide 44: Further Observational Studies Add Complexity
History
Patients with higher creatinine on hemodialysis have less death. (AJKD 15:471, 1990)
URR and outcome (NDT 12: 1987)
No difference in survival using Kt vs. Kt/V (Lowrie 2002)
These and other observations set the stage for a randomized trial on “high” vs. “low” dialysis dose defined by Kt/V; hence the HEMO trial.
Dialysis Core Curriculum 2021

## Slide 45: 2002 HEMO Study: “High” vs. “Low” Kt/Vurea
Adapted from Eknoyan G. et al. N Engl J Med 347:2010-2019, 2002
Patients at Risk
Standard Dose 854 759 630 524 451 382 315 253 197 149
High Dose 857 753 637 538 470 399 327 266 219 166
Months of Follow-up
Patients Surviving (%)
0
6
12
18
24
30
36
42
48
54
60
40
50
60
70
80
90
100
Standard Dose
High Dose
(spKt/V=1.32; 190 min)
(spKt/V=1.71; 219 min)
Dialysis Core Curriculum 2021
Notes: 45

## Slide 46: HEMO Trial Problem: Lack of Separation only 30% increase in Kt/Vurea and 15% increase in treatment time
Variable | Standard Dose Group | High Dose Group
spKt/Vurea | 1.32 + 0.09 | 1.71 + 0.11
eKt/Vurea | 1.16 + 0.08 | 1.53 + 0.09
Urea Reduction Ratio | 66.3 + 2.5 % | 75.2 + 2.5 %
Pre-dialysis Urea | 62.1 + 13.6 mg/dl | 54.3 + 11.8 mg/dl
Treatment Time | 190 + 23 minutes | 219 + 23 minutes
Beta2-microglobulin clearance | 3.5 + 3.6 L | 4.0 + 3.6 L
HISTORY
Adapted from Table 2 in Eknoyan G. et al. N Engl J Med 347:2010-2019, 2002
Dialysis Core Curriculum 2021

## Slide 47: Further Studies Have Not Clarified This Issue
Frequent Hemodialysis Network Trials
  Daily HD trial showed surrogate, 1-year mortality benefit for 5.3 treatments per week vs. 3 treatments per week
  Nocturnal HHD trial failed to recruit adequate study size
TIME Trial
  Attempted to examine dialysis time in incident patients
  Ended at 1.1 years due to lack of separation (207 min vs. 216 min)
Ademex Trial in Peritoneal Dialysis
  Similar to HD, improving urea clearance measured by urea kinetics showed no mortality benefit
However, renewed focus on salt and water removal and balance may impact outcomes when combined with urea clearance and dialysis time.
History
FHN Trial Group. N Engl J Med 363:2287-2300, 2010; FHN Nocturnal Trial Group. Kidney Int 80:1080-1091, 2011;
Paniagua R et al. J Am Soc Nephrol 13: 1307-1320, 2002; Dember LM et al. J Am Soc Nephrol 30:890-903, 2019
Dialysis Core Curriculum 2021

## Slide 48
Scientific Background
Assessing Adequacy
Dialysis Core Curriculum 2021

## Slide 49
What Is Kt/Vurea? A Unitless “Dose” of Dialysis
time
Plasma
Urea
Dialysis
Kt/Vurea
nPCR
Kt/Vurea
Dialysis
K=Clearance of urea (ml/min)
t=Dialysis time (min)
V=Volume of Distribution of Urea (L)
Dialysis Core Curriculum 2021

## Slide 50: What Is the Normalized Protein Catabolic Rate (nPCR)?
In a stable patient, measurement of urea generation is an index of protein catabolism reflecting protein intake and can provide assistance with dietary management.
nPCR =
5420 x Urea Generation rate (mg/min)
Urea Volume of Distribution (ml)
+ 0.17
Based on observational studies:
nPCR =
Second Predialysis BUN – First Postdialysis BUN
Time interval between dialysis sessions
5420 x
This does not consider:
Residual renal function (lowers BUN)
Volume changes between dialysis sessions (lowers BUN)
Urea generation during dialysis
Dialysis Core Curriculum 2021

## Slide 51: What Is Equilibrated Kt/V (eKt/V)?
Treatment Time
Kt/Vurea
spKt/V
eKt/V
Post BUN measured after hemodialysis to account for rebound
Hence, eKt/V will generally be lower than spKt/V at typical hemodialysis treatment times.
Dialysis Core Curriculum 2021

## Slide 52
Comparing Different Dialysis Prescriptions: “Standardizing” the Kt/Vurea
Developed by Frank Gotch to give an equivalent clearance based on a on a steady state concentration of urea. Nephrol Dial Transplant 13 suppl 6:10-14, 1998
This allows a comparison of any hemodialysis prescription schedule.
The typical 3 times-a-week hemodialysis schedule with a single-pool Kt/V of 1.2 yields a weekly standardized Kt/V of approximately 2.0-2.1.
Dialysis Core Curriculum 2021

## Slide 53: Standardized Kt/Vurea (std Kt/V)
Scientific Background
10080 (1-e-eKt/V)
t
(1-e-eKt/V)
spKt/V
+
10080
N x t
- 1
stdKt/V =
Daugirdas J. J Am Soc Nephrol 1993
Dialysis Core Curriculum 2021

## Slide 54
Clinical Definitions
Assessing Adequacy
Dialysis Core Curriculum 2021

## Slide 55: Adequate Hemodialysis
Control of Uremic Symptoms
Good Nutritional Status
Control of Electrolytes and Acid-Base Status
Blood Pressure Control
Physical Activity
Residual Renal Function – remains the strongest marker for mortality in all forms of dialysis therapy
Clinical Definitions
Dialysis Core Curriculum 2021

## Slide 56
Regulatory Definitions
Assessing Adequacy
Dialysis Core Curriculum 2021

## Slide 57: Target Kt/Vurea Metrics
Beginning in approximately 2000 with the Kidney Dialysis Outcomes Quality Initiative, multiple professional societies have published guidelines on hemodialysis urea kinetic goals. These are largely based on observational studies and expert opinion.
Starting in 2012, the Center for Medicare and Medicaid Services (CMS) tied achieving urea removal goals to reimbursement to dialysis in the ESRD Quality Incentive Program (QIP).
  2012-2014: the measurement was URR
  2015-Current: the measurement is Kt/V
Regulatory Definitions
Dialysis Core Curriculum 2021

## Slide 58: Regulatory Targets for Urea Removal
ESRD Quality Incentive Program
Monthly single-pool Kt/Vurea measurement in adult patients
Includes all patients receiving hemodialysis more than twice a week and less than 4 times a week
Denominator is patient treatment-months
Regulatory Definitions
https://www.cms.gov/Medicare/Quality-Initiatives-Patient-Assessment-Instruments/ESRDQIP/06_MeasuringQuality. Accessed October 22, 2020
Dialysis Core Curriculum 2021

## Slide 59
McCausland FR, Waikar SS, Brunelli SM: Increased dietary sodium is independently associated with greater mortality among prevalent hemodialysis patients. Kidney Int 82(2):204-211, 2012
Kovesdy CP, Regidor DL, Mehrotra R: Serum and dialysate potassium concentrations and survival in hemodialysis patients. Clin J Am Soc Nephrol 2(5):999-1007, 2007
Rachoin JS, Weisberg LS: How should dialysis fluid be individualized for the chronic hemodialysis patient? Potassium. Sem Dial 21(3):223-225, 2008
De Nicola L, Bellizzi V, Minutolo R, et al: Effect of dialysate sodium concentration on interdialytic increase of potassium. J Am Soc Nephrol 11(12):2337-2343, 2000
Zehnder C, Gutzwiller JP, Huber A, et al: Low-potassium and glucose-free dialysis maintains urea but enhances potassium removal. Nephrol Dial Transplant 16: 78-84, 2001
Martin RS, Panese S, Virginillo M, et al: Increased secretion of potassium in the rectum of humans with chronic renal failure. Am J Kidney Dis 8(2):105-110, 1986
Sandle GI, Gaiger E, Tapster S, et al: Evidence for large intestinal control of potassium homoeostasis in uraemic patients undergoing long-term dialysis. Clin Sci Lon 73(3):247-252, 1987
Choi HY, Ha SK: Potassium balances in maintenance hemodialysis. Electrolyte Blood Press 11:9-16, 2013
Oreopoulos DG, Khanna R, Williams P, et al: Continuous ambulatory peritoneal dialysis – 1981. Nephron 30(4): 293-303, 1982
Blumberg A, Roser HW, Zehnder C, et al: Plasma potassium in patients with terminal renal failure during and after haemodialysis; relationship with dialytic potassium removal and total body potassium. Nephrol Dial Transplant 12(8):1629-1634, 1997
REFERENCES
Dialysis Core Curriculum 2021

## Slide 60
Skrabal F, Dittrich P, Gabl F: Calcium uptake and phosphate removal during hemodialysis with variing dialysate calcium. Klin Wochenschr 52(6):266-271, 1974
Musci I, Hercz G, Uldall R, et al: Control of serum phosphate without any phosphate binders in patients treated with nocturnal hemodialysis. Kidney Int 53(5):1399-1404, 1998
Hou SH, Zhao J, Ellman CF, et al: Calcium and phosphorus fluxes during hemodialysis with low calcium dialysate. Am J Kidney Dis 18(2):217-224, 1991
Karohl C, de Paiva Paschoal J, de Castro MC, et al: Effects of bone remodelling on calcium mass transfer during haemodialysis. Nephrol Dial Transplant 25(4):1244-1251, 2010
Eknoyan G, Beck GJ, Cheung AK, Daugirdas JT, et al: Effect of dialysis dose and membrane flux in maintenance hemodialysis. N Engl J Med 347(25) :2010-2019, 2002
FHN Trial Group, Chertow GM, Levin NW, et al: In-center hemodialysis six times per week versus three times per week. N Engl J Med 363(24) :2287-2300, 2010
FHN Nocturnal Trial Group, Michael V Rocco, Robert S Lockridge Jr, et al: The effects of frequent nocturnal home hemodialysis: the Frequent Hemodialysis Network Nocturnal Trial. Kidney Int 80(10): 1080-1091, 2011
Paniagua R, Amato D, Vonesh E, et al: Effects of increased peritoneal clearances on mortality rates in peritoneal dialysis: ADEMEX, a prospective, randomized, controlled trial. J Am Soc Nephrol 13(5): 1307-1320, 2002
Dember LM, Lacson E Jr, Brunelli SM, et al. The TiME Trial: A Fully Embedded, Cluster-Randomized, Pragmatic Trial of Hemodialysis Session Duration. J Am Soc Nephrol 30(5):890-903, 2019
https://www.cms.gov/Medicare/Quality-Initiatives-Patient-Assessment-Instruments/ESRDQIP/06_MeasuringQuality. Accessed October 22, 2020
REFERENCES
Dialysis Core Curriculum 2021