## Slide 1: Basic Principles of Uremic Toxicity and Uremic Toxin Removal: Hemodialysis
Raymond C. Vanholder, MD, PhD
University Hospital Ghent Belgium
Dialysis Core Curriculum 2021

## Slide 2: Raymond C. Vanholder
  Consultancy: Nextkidney Project; Kibow; Jafron; BBraun; Baxter Healthcare; Fresenius Medical Care
  Scientific Advisor/Membership: European Kidney Health Alliance; International Scientific Advisory Board Dutch Kidney Foundation; J Am Soc Nephrol; Nephrol Dial Transplant; NRN Reviews Nephrol
Disclosures
Dialysis Core Curriculum 2021

## Slide 3: Learning Objectives
Describe the effects of hemodialysis and related strategies
Explain the basic classification of uremic toxins
Discuss how conventional hemodialysis and hemodiafiltration work, including their effect on uremic solute removal
Describe alternative modes of removal that have recently been developed or are under development
Dialysis Core Curriculum 2021

## Slide 4: Aims of Hemodialysis
Restore volume status (fluid removal): mainly acute (short term) impact on outcomes
Restore electrolyte balance: mainly acute (short term – sodium, potassium) or mainly chronic (long term – phosphate, bicarbonate) impact on outcomes
Remove uremic retention solutes: mainly chronic (long term) impact on outcomes
Dialysis Core Curriculum 2021
Notes: This slide illustrates the aims of dialysis: restoring volume status with mainly acute impact, electrolyte balance with mixed acute and chronic impact (sodium, potassium, phosphate, bicarbonate), and removal of uremic retention solutes (in case of a known biological or biochemical impact called uremic toxins) which mainly have a chronic effect, e.g. by promoting cardiovascular morbidity and mortality.

## Slide 5: Classification of Uremic Toxins
Small water soluble compounds (prototypes urea and uric acid): MW <500 Dalton; easily removed by any type of hemodialysis
Protein bound compounds (prototypes indoxyl sulfate, p-cresylsulfate): mostly MW <500 Dalton; difficult to remove by any type of hemodialysis
Middle molecules (prototypes β2-microglobulin, interleukins): MW >500 Dalton; only removed by hemodialyszers with large enough pore size (high flux)
Dialysis Core Curriculum 2021
Notes: Based on removal by hemodialysis, the most classical subdivision of uremic toxins is along these three types of which the dialysis-related characteristics are also depicted in the slide. The problem of removal of protein bound compounds is that their protein binding (mostly to albumin) hampers their removal, as only the free (unbound) fraction is available for removal. Thus, the more important protein binding is, the more difficult dialysis removal becomes. The toxicity of these compounds will be described more in detail in parts 2 to 4 of this set of presentations. At the end of part 4, we will also propose a classification of toxins in function of the evidence of their toxicity.

## Slide 6: Current Hemodialysis Modes
Dialysis Core Curriculum 2021
Notes: We will start by explaining the principles of the currently most frequent hemodialysis removal modes: diffusion and convection.

## Slide 7: Diffusion vs. Convection
Dialysis Core Curriculum 2021
Diffusion is the basic principle of hemodialysis; hereby, solutes move through a semi-permeable membrane from the area with the highest concentration (in dialysis for most molecules the blood side) to the area with the lowest concentration (for most molecules the dialysate side). Diffusion is essentially useful for removal of small molecules.
Convection is the basic principle of hemofiltration; hereby, a large volume of plasma water is pushed through the semipermeable membrane and with this volume also molecules in that plasma are dragged to the other side (from the Latin convehere – to drag). The volume that is filtered out of the plasma is replaced by an equivoluminous volume of substitution fluid containing electrolytes but no toxins keeping the volume status stable. Practically, if one puts a teabag in hot water without doing anything else, the brown color that escapes from the bag does so by diffusion. However, if one starts dragging the bag through the water, this is on the basis of convection. Generally, this procedure allows more brown color to escape. Convection is useful to remove large molecules. In hemodiafiltration, diffusion and convection are combined.

## Slide 8: Impact of Low-Flux Dialysis on Various Types of Uremic Toxins
Dialysis Core Curriculum 2021
Only the small-water soluble compounds cross easily the membrane. Also, some of the protein bound componds pass the membrane if they are free (unbound). The protein bound compounds which are bound to albumin, however, do not cross the membrane and are reflected, in the same way as the middle molecules.

## Slide 9: Effect of High-Flux Dialysis on Various Types of Uremic Toxins
Dialysis Core Curriculum 2021
Not only the small water soluble compounds and the free protein bound compounds, but also the middle molecules cross the membrane. The protein bound compounds which are bound to albumin, however, do still not cross the barrier and are reflected. Whereas removal of middle molecules is more efficient than with low-flux, removal of small water soluble compounds and protein-bound compounds is virtually the same.

## Slide 10: Effect of Hemodiafiltration on Various Types of Uremic Toxins
Dialysis Core Curriculum 2021
The middle molecules are removed even more efficiently than with high-flux hemodialysis. Also the protein bound compounds which are bound to their binding protein are now removed somewhat more efficiently. Small water soluble compounds roughly are removed in the same way as with the two other strategies.

## Slide 11: Uremic Solute Kinetics Has a Major Impact on Removal
Dialysis Core Curriculum 2021
Eloot et al, NDT, 27, 4021-4029, 2012
From the moment dialysis starts, the dialyzer starts purifying the plasmatic volume, which results in mass transfer (MT) into the dialysate.
From the moment solute concentration decreases in the plasma, also diffusion of solutes from the extraplasmatic to plasmatic volume starts. This process is symbolized by K12 (clearance from compartment 2 (extraplasmatic) to compartment 1 (plasmatic)).
However, the shift of solutes from extraplasmatic to plasmatic is slower than the one from plasma to the dialysate. As a consequence, concentration in the plasma decreases more quickly than the extraplasmatic concentration, but a lower plasmatic concentration also means less solute available for diffusion and thus lower mass transfer and efficiency of dialysis. This phenomenon also gives rise to rebound after dialysis, as after the end of dialysis, solute continues to move from extraplasmatic to intraplasmatic. Thus, solute concentration after dialysis rises very quickly so that part of the removal effect is lost. The shorter dialysis is, the more pronounced this compartment disbalance and rebound will be.

## Slide 12: Effect of Kinetics on Solute Concentration
Dialysis Core Curriculum 2021
Vanholder et al, KI, 88, 460-465, 2015
In general, removal by dialysis is easier from the plasmatic compartment than from extraplasmatic, as there is almost always some degree of resistance against the shift of solutes from extraplasmatic (correspondoing to tissues and organs, where often toxicity is exerted) to intraplasmatic. As a consequece, tissue concentration lags behind on plasma concentration. At the beginning of dialysis, removal is essentially limited to plasma, without equivalent refilling from extraplasmatic, and there is thus a steep concentration decline. However, after some time, the extraplasmatic compartment catches up and starts to refill the plasma, and both concentration curves run more or less in parallel, however without coming together. At the end of dialysis, the shift from extraplasmatic, where concentration is higher, to plasma continues, resulting in a rebound. The higher the resistance against a shift from extraplasmatic to plasma, the more both curves will be apart, and the higher the rebound, which is more or less a mirror image of the steep decline at the start of dialysis.

## Slide 13: Impact on Different Time Schedules on Solute Removal
Dialysis Core Curriculum 2021
Notes: In this slide, we illustrate the effect of different dialysis timeframes on the concentration in the plasmatic (thick lines) and the extraplasmatic compartments (thin lines) of molecules with a multicompartmental distribution. A situation is described whereby we start from a standard alternate day (3 to 4 hrs) regime (blue). There is a steep decline of plasma concentration during the initial phase of dialysis, but due to a loss of mass transfer, this effect is attenuated later during dialysis. Dialysis is followed by a marked rebound, after which concentration continues to rise gradually until immediately before the next dialysis, when it reaches more or less the same level as before the first dialysis. Concentration in the extraplasmatic compartment is markedly lagging behind that in the plasma which hampers mass transfer. The next illustration (green) is that of low efficiency extended alternate day dialysis (8 hours, blood flow 200 mL/min). The initial decline in concentration in plasma is less steep but more consistent than with the standard regime (blue) and is continued for a longer period. Removal as a consequence is more important and there is less rebound at the end of dialysis, because the slower removal over longer time allows the extraplasmatic compartment to better keep pace with the plasmatic compartment. The concentration rise till the next dialysis is less important than with the shorter regime. Removal from the extraplasmatic compartment is also more efficient. This is a nice illustration of the impact of dialysis length on solute removal (discussed further in part 4 on middle molecules). The last illustration is focusing on daily short (2 hr) dialysis (magenta). Now dialysis stops near the end of the steep phase of the decline in plasma concentration. There is less time in between dialyses for concentration to rise again, and due to the fast succession of sessions, concentration pre-dialysis gradually declines. Although extraplasmatic concentration is lagging behind, again due to the succession of sessions, a gradual decline of extraplasmatic concentration also takes place.

## Slide 14: Alternative Modes for Dialytic Solute Removal
Dialysis Core Curriculum 2021

## Slide 15: Medium Cut-Off Membranes Increase Removal of Large “Middle” Molecules
Dialysis Core Curriculum 2021
Kirsch et al, NDT, 32: 165–172, 2017
Extremely open membranes with large pores (larger than high flux membranes – MCO or Medium Cut-off membranes) allow the removal of larger middle molecules. These membranes were first developed for the treatment of patients with multiple myeloma but were soon thereafter also tested in end stage kidney failure. Removal of immunoglobulin free light chains is markedly superior for the open membranes as compared to high flux. Middle molecule removal by the open membranes in dialysis mode was comparable or even superior to hemodiafiltration with >23L substitution fluid. The reason is internal hemodiafiltration which is proper to all large pore membranes but becomes more important as pore size becomes more important. Due to positive hydrostatic pressure at the dialyzer inlet, water with molecules is ultrafiltered but albumin to a large extent remains in the blood stream, increasing colloid osmotic pressure, which at a certain point in the dialyzer exceeds hydrostatic ultrafiltration pressure. From that moment on, dialysis water is attracted back to the blood stream, which practically mimicks a classical hemodiafiltration pattern. Improved removal with this type of membrane is essentially restricted to middle molecules, especially the larger ones.

## Slide 16: Adsorption: Catching Uremic Solutes
Dialysis Core Curriculum 2021
Tijink et al, Biomaterials, 34(32):7819-28; 2013
In adsorption, sorbents like active coal are used with the intention to catch uremic toxins. This approach mostly affects concentration of charged molecules, essentially protein bound solutes and middle molecules. Adsorption of non-charged molecules like urea is more difficult. Sorbents can be used to remove toxins at the blood side of the dialyzer or at the dialysate side. Tijink et al in Biomaterials offers an example of an in vitro study where sorbent was embedded unto a classical high flux dialysis membrane and removal of protein bound indoxyl sulfate was studied. Removal as precent concentration decline compared to 4 hrs PES/PVP as standard (Ct/C0 = 1.0, which equals 100%). By adding sorbent to the membrane, at four hours, an additional decrease of indoxyl sulfate by >80% is observed as compared to membrane alone.

## Slide 17
Dialysis Core Curriculum 2021
Meijers et al, Artif Organs, 32: 214-219; 2008
Adsorption: Catching Uremic Solutes
The sorbent can also be applied at the dialysate/ultrafiltrate side. In a pilot experiment in 3 patients, a combination of fractionated plasma separation + adsorption followed by reinfusion of the cleaned plasma filtrate (full lines) is compared to hemodialysis for relative removal of p-cresol (a surrogate for protein bound p-cresyl sulfate). In the clinic, this strategy is essentially used as artificial liver. Removal is almost doubled by the sorption technique, offering proof of concept of removal of uremic toxins by adsorption. However, a downside of this experiment was the frequent occurrence of clotting complications (in CKD patients), so that to our knowledge, this technique is currently not applied clinically as a dialysis technique (only in liver failure where coagulation is more suppressed than in CKD).

## Slide 18
Dialysis Core Curriculum 2021
Gura et al, JCI Insight, 1, 2016, doi: 10.1172/jci.insight.86397
Adsorption: Catching Uremic Solutes
Sorbents can also be used at the dialysate side to catch uremic toxins and regenerate dialysate. This method is currently used and tested in prototypes of wearable artificial kidney (WAK), like the system above developed by Gura et al, or portable articficial kidney (PAK). In this setting, the sorbent is not used to increase removal, but to cleanse dialysate so that it can be recirculated in a closed loop system, dramatically decreasing the volume of dialysate needed and allowing to develop wearable or portable and thus more flexible systems. Some of these systems have reached the phase of pilot experimental studies (phase 2). This technique is described more extensively in this series in the presentation by Dr. A. Davenport, entitled: “Translational and transformative dialysis: wearable and bioartificial kidney.”

## Slide 19: Bio-Artificial Kidney: Applying Biology to Remove Uremic Toxins
Dialysis Core Curriculum 2021
Buffington et al, Transl Res, 163:342-351; 2014
Another concept that is currently under development is bio-artificial kidney. Here, dialyzer membranes are seeded with kidney tubule cells containing organic anion transporters (OATs), which are pump systems actively transporting uremic toxins from the blood to the dialysate site, conform their function in the kidneys. These systems are still at an experimental stage. Also, this technique is described more in depth in Dr. A. Davenport’s contribution.
In the bioartificial renal epithelial cell system (BRECS) extracorporeal circuit schematic for future clinical treatment of acute renal failure, blood from the patient flows through a standard dialysis hemofilter, with ultrafiltrate (UF) generated by the hemofilter being directed through the BRECS. The 65-kDa molecular weight cutoff of the hemofilter provides immunoprotection to the cells in the BRECS from any immunoreactive molecules and/or cells from the patient. “Conditioned” UF containing BRECS cellular therapeutic products passes from the BRECS and is channeled back to the blood returning to the patient. Before being merged with the returning blood, the conditioned UF passes through an immunoisolation filter (I-Filter), which protects the patient from any large molecular by-products and/or cells released by the BRECS that could cause an adverse reaction.

## Slide 20: Conclusions
Adequacy of removal of uremic solutes is hampered by characteristics of dialyzers and dialysis and by the multicompartmental distribution of most uremic toxins.
Removal can be enhanced by opening pore size and adding convection, but also by applying extended or frequent dialysis.
Novel concepts that are currently developed or tested include extremely open dialysis membranes, adsorption and bio-artificial kidney.
Dialysis Core Curriculum 2021